## Slide 1: GIS and RS for Forest Resource Assessment
Kefyalew Sahle Hawassa University
Wondo Genet College of Forestry and Natural Resources
GIS Department

## Slide 2: Unit 1. Introduction

## Slide 3: 1. Introduction
1.1. Overview of Optical, Microwave, RADAR LiDAR, and thermal remote sensing for forest resources assessment
1.2. Use and importance of RS & GIS in forest identification and measurement
1.3 General application of RS and GIS in forestry

## Slide 4: Overview of remote sensing for forest resources assessment
Sensor characteristics on the basis of whether the sensor operates
  in the visible and infrared spectral domain (multispectral) or
  in the microwave spectrum (SAR).
This distinction determines whether imagery can be acquired independent of solar illumination and cloud cover.

## Slide 5: Overview of remote sensing for forest resources assessment
Multispectral sensors
  measure the reflected sunlight, and as such obviously depend on there being sufficient incident solar illumination and absence of cloud cover.
  This is important not only for instantaneous acquisitions but also for the creation of consistent time series, for example to compare data over several crop seasons.

## Slide 6: Overview of remote sensing for forest resources assessment
SARs
  measure the backscattered radiation from a microwave pulse emitted by the SAR itself, thus independently of solar illumination.
  For lower frequencies (C- and L-band), SARs are usually insensitive to atmospheric conditions, except in case of intensive rain events.
One of the SAR’s strengths is its capacity to ensure consistency in the acquisition of time series for use in crop delineation and area measurement.
This is especially true for the Sentinel-1A and -1B instruments, which combine a spatial resolution of 10 m with a revisit frequency of six days.

## Slide 7: Overview of remote sensing for forest resources assessment
Sensor characteristics on the bases of spatial resolution.
ESA denomination relies upon the practical
  < 4 m,
  4–10 m,
  10–30 m,
  30–300 m and
  > 300 m resolution ranges to group families of sensors.

## Slide 8: Overview of remote sensing for forest resources assessment
Sensor availability
  under free and open licenses and
  those categories (<10 m) that fall within the commercial realm.

## Slide 9: Selected Earth-Observing Satellites (1/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
MSS | Landsat 1–5 | VNIR | 80 (60) | 4
TM | Landsat 4–5 | VNIR | 30 | 6
 |  | Thermal | 120 | 1
ETM+ | Landsat 7 | Panchromatic | 15 | 1
 |  | VNIR | 30 | 6
 |  | Thermal | 60 (30) | 1
OLI | Landsat 8 | Panchromatic | 15 | 1
 |  | VNIR | 30 | 6
 |  | SWIR | 30 | 2
TIRS |  | Thermal | 100 | 2

## Slide 10: Selected Earth-Observing Satellites (2/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
OLI | Landsat 9 | Panchromatic | 15 | 1
 |  | VNIR | 30 | 6
 |  | SWIR | 30 | 2
TIRS |  | Thermal | 100 | 2
Hyperion | EO-1 | Hyperspectral | 30 | 220
 |  | Panchromatic | 10 | 1
ALI |  |  |  | 
 |  | VNIR | 30 | 9
ASTER | Terra | VNIR | 15 | 3
 |  | SWIR | 20 | 6
 |  | Thermal | 90 | 5

## Slide 11: Selected Earth-Observing Satellites (3/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
– | RapidEye | VNIR | 5 | 5
– | EROS-A | Panchromatic | 1.9 | 1
– | EROS-B | Panchromatic | 0.7 | 1
– | Pléiades 1A | Panchromatic | 0.7 (0.5) | 1
 |  | VNIR | 2 | 4
– | Pléiades 1B | Panchromatic | 0.7 (0.5) | 1
 |  | VNIR | 2 | 4
HRV | SPOT 1–3 | Panchromatic | 10 | 1
 |  | VNIR | 20 | 3
HRVIR | SPOT 4 | Panchromatic | 10 | 1
 |  | VNIR | 20 | 3
 |  | SWIR | 20 | 1

## Slide 12: Selected Earth-Observing Satellites (3/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
HRS | SPOT 5 | Panchromatic | 10 | 1
HRG |  | Panchromatic | 5 (2.5) | 2
 |  | VNIR | 10 | 3
 |  | SWIR | 20 | 1
NAOMI | SPOT 6–7 | Panchromatic | 1.5 | 1
 |  | VNIR | 6 | 4
AVNIR-2 | ALOS | Panchromatic | 2.5 | 1
 |  | VNIR | 10 | 4
MSI | Sentinel-2a and b | VNIR | 10/20/60 | 10
 |  | SWIR | 20/60 | 3
– | IKONOS | Panchromatic | 1 | 1
 |  | VNIR | 4 | 4

## Slide 13: Selected Earth-Observing Satellites (5/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
– | Quickbird | Panchromatic | 0.6 | 1
 |  | VNIR | 2.5 | 4
– | Geoeye | Panchromatic | 0.4 | 1
 |  | VNIR | 1.65 | 4
– | Worldview-1 | Panchromatic | 0.5 | 1
– | Worldview-2 | Panchromatic | 0.46 | 1
 |  | VNIR | 1.85 | 8
– | Worldview-3 | Panchromatic | 0.31 | 1
 |  | VNIR | 1.24 | 8
 |  | SWIR | 3.7 | 8
 |  | CAVIS | 30 | 12
KH1–KH6 | CORONA/ARGON/LANYARD | Panchromatic | &lt;1.8 | 1

## Slide 14: Selected Earth-Observing Satellites (6/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
– | Formosat-2 | Panchromatic | 2 | 1
 |  | VNIR | 8 | 4

## Slide 15: Selected Earth-Observing Satellites (7/7)
Sensors | Platform | Spectrum | Spatial Resolution (m) | Spectral Bands
ASAR | Envisat | Microwave | 30 | 2
SAR | ERS-1 and 2 | Microwave | 30 | 1
SAR | RADARSAT-1 | Microwave | 8/30/50/100 | 1
SAR | RADARSAT-2 | Microwave | 2/5/16/30/50/100 | 1
SAR | Sentinel-1 | Microwave | 5/20/40 | 1
– | COSMO-Skymed | Microwave | 1/3/15/16/20 | 1
– | TerraSAR-X | Microwave | 01-03-18 | 1

## Slide 17: 1.2 Use and importance of RS & GIS in forest identification and measurement
RS and GIS are used for
  Observation
  Analysis and measurement
  Mapping
  Monitoring over time and space
  Decision support

## Slide 18: 1.2 Use and importance of RS & GIS in forest identification and measurement
Observation
  detection and identification of features such as a specific type of habitat or events such as fires or storms
Analysis and measurement
  measure a number of biological and physical variables such as elevation, productivity, cloud type and coverage, land and water surface temperature, precipitation amount, wind velocity, and water quality.
  input to a variety of models including those used for species, population, and ecosystem analysis

## Slide 19: 1.2 Use and importance of RS & GIS in forest identification and measurement
Observation
  detection and identification of features such as a specific type of habitat or events such as fires or storms
Analysis and measurement
  measure a number of biological and physical variables such as elevation, productivity, cloud type and coverage, land and water surface temperature, precipitation amount, wind velocity, and water quality.
  input to a variety of models including those used for species, population, and ecosystem analysis
Mapping
  Generate various forest related thematic maps
  E.g. forest cover map
  Forest cover change map
  process is a common way to benefit from its capabilities.

## Slide 20: 1.2 Use and importance of RS & GIS in forest identification and measurement
Monitoring over time and space
  to monitor how they change over time
  important for documenting how features have changed in the past, and predicting changes into the future.
Decision support
  Incorporating remotely sensed data into the decision-making process is a common way to benefit from its capabilities.

## Slide 21: Categories of forest information obtained from remotely sensed data (e.g.)
detailed forest inventory data (e.g., within-stand attributes)
broad area monitoring of forest health and natural disturbances
assessment of forest structure in support of sustainable forest management

## Slide 22: Remote sensing and GIS to forestry
With forest management becoming increasingly complex, due to greater environmental and social involvement and pressures, GIS is likely to play an increasingly central role.
Developments in greater band width, web based technology and wireless communication will provide much greater opportunities for information access even in more remote areas.
This will allow real time online data capture and query in the field.

## Slide 23: GIS to forestry
Strengthen Forest Management
  GIS it answers crucial questions that help foresters in forest management departments such as condition, location, modelling and trends make decisions.
GIS application in forest management
  GIS for strategic planning and modeling
  Map production
  Fire management
  Harvest planning
  Resource Management

## Slide 24: GIS to forestry
Increase Business Value, Efficiency, and Productivity
  GIS bring your organization’s forest data together on a centralized platform.
  Staff members can easily search data, see it with a map viewer, bring it into their projects, and analyze it using powerful tools and models

## Slide 25: GIS to forestry
Improve Manufacturing Returns
  Create a common operational picture for coordinating production and distribution activities.
  Monitor facilities and operations in real time including production levels, downtime, and costs.

## Slide 26: General application of RS and GIS in forestry
Detailed forest inventory data
Forest health and natural disturbances
Insect disturbance
Fire
Landscape ecology, habitat, and biodiversity

## Slide 28: Summary of the application of remote sensing systems
The applications of the following remote sensing systems in forestry were reviewed.
  Photographic (Air)
  Scanning (Air & Space)
  Radar (Air & Space)
  Lidar (Laser) (Air)
  Videography (Air)

## Slide 29: Applications of Aerial Photography in Forestry - Mapping (qualitative)
Forest cover types
Identify individual species
Species composition
Forest fire detection
Forest fire hazard
Detecting forest trees health (vigor and stress) forest trees diseases and insects infestation forest trees under air, soil and water pollution
Assessment of wind damage and other sever climatic condition Detecting deforestation and forest degradation
Forest monitoring:
  some of the above logging activities
  reforestation and afforestation
Timber harvesting planning
Forest roads planning
Forest inventory Forest management
Assessing slope failure and soil erosion
Assessing and managing forest recreation resources
Assessing and managing wildlife habitat

## Slide 30: Applications of Aerial Photography in Forestry - Measurements and estimation (quantitative)
Forest cover area measurement
Number of trees
Tree height measurement
Crown cover measurement
Crown closure measurement
Crown diameter measurement
DBH estimation
Age estimation Site estimation
Timber volume estimation
Thinning volume estimation
Basal area estimation
Annual Growth estimation
Basal area growth estimation
Biomass estimation
Stand size
Dead, declined trees

## Slide 31: Applications of Aircraft & Satellite Scanning Sensor System (MSS) in Forestry - Mapping (qualitative)
Forest cover types
Identify individual species
Forest fire detection
Forest fire hazard
Detecting forest trees health (vigor and stress) forest trees diseases and insects infestation forest trees under air, soil and water pollution
Assessment of wind damage and other sever climatic condition
Detecting deforestation and forest degradation
Forest monitoring:
  some of the above logging activities
  reforestation and afforestation
Timber harvesting planning
Forest roads planning
Assessing slope failure and soil erosion
Assessing and managing forest recreation resources
Assessing and managing wildlife habitat

## Slide 32: Applications of Aircraft & Satellite Scanning Sensor System (MSS) in Forestry - Measurements and estimation (quantitative)
Forest cover area measurement
Tree height estimation
Crown cover estimation
DBH estimation
Age estimation
Timber volume estimation
Basal area estimation
Biomass estimation
.

## Slide 33: Applications of Aircraft and Satellite Radar System in Forestry - Mapping (qualitative)
Forest cover types
Forest species level mapping
Mapping flooded forest
Detecting deforestation and forest degradation
Monitoring logging activities
Detecting forest roads
Mapping burned forest
.

## Slide 34: Applications of Aircraft and Satellite Radar System in Forestry - Measurements and estimation (quantitative):
Forest cover area measurement
Tree height estimation
Crown cover estimation
DBH estimation
Number of trees per unit area (density)
Age estimation
Timber volume estimation
Basal area estimation
Biomass estimation
.

## Slide 35: Applications of Lidar (Laser) System in Forestry
Tree height estimation.
Forest cover types determination.
Forest trees species differentiation.
Crown cover or canopy density estimation.
Forest stands volume estimation.
Forest stands woody biomass estimation.
Forest trees water stress detection.
Forest trees nutrient deficiency

## Slide 36: Applications of Aerial Videography in Forestry
Forest cover types determination.
Forest trees species differentiation.
Crown cover or canopy density estimation.
Detecting forest trees health (vigor and stress) forest trees diseases and insects infestation
Mapping forest trees spatial distribution